1	Vdd
2	Vss
3	CS	Chip select Only for first chip, rest controlled by token. Active high
4	SDI	SPI data In All chips paralleled
5	SCK	SPI Clock All chips paralleled
6	TCK	Token Clock All chips paralleled. Positive edge moves token.
7	WR	Write/Read. 1=read, 0=write
8	EN	Count Enable Gate for counting interval
9	SDAC	On-chip DAC program when 1 (set to 0)
10	RST	Global reset 0 to reset
11	Vddd
12	ssd
13	Vdd
14	Vss
15	VH2	Scaler2 window discriminator High (i2c dac)
16	VL2	Scaler2 window discriminator Low (i2c dac)
17	VH1	Scaler1 window discriminator High (i2c dac)
18	VL1	Scaler1 window discriminator High (i2c dac)
19	VL0	Scaler0 threshold discriminator (i2c dac)
20	BDAC	On-Chip DAC range control
21	BLN	Output baseline control
22	BLK	Input leakage current control
23	OAN	Analog pulse output
24	OLK	Pixel leakage current monitor
25	Vss
26	Vdd
27	CAL	Test pulse input
28	Vsubd
29	SDO	SPI Data Out
30	TO	Token out Input. Want to know that token went all the way through.
31	E4T	N/A
32	Vddd
33	Vssd
34	Vss
35	Vdd

7 digital control signals. 1 SPI data port (3 signals). Token passing for multiple chip
installations.

We will not implement BDAC, BLN or BLK. We'll only use the off-chip DACs
(5 channels).