# Germanium detector IOC (Maia electronics)
The general idea of this IOC is to provide a set of PVs which falls naturally into a scanning experiment. The counting logic is therefore based on the synApps Scaler record and uses most of it’s logic. There are many additional Pvs which deal with the details of the configuration of the ASICs, monitoring of signals and displaying summary data.
The hardware consists of an embedded processor in the detector interface module, which runs Debian Linux. Applications are developed in the embedded system, and natively compiled there.
The high-speed data is handled by a ZeroMQ server which resides in the embedded system. This accepts data as it is streamed out of the module’s FPGA fabric and publishes it to whoever subscribes to it. A client on a host computer subscribes to it

Routines in devzDDM.c:
void frame_done(int signum)
This is the interrupt service routine. When the detector is told to count, it sets a hardware timer in the fabric. When the timer expires, it causes an interrupt which is directed to this routine.

int decode(unsigned char *buf, int len, zDDMRecord *psr)
this decodes the packed binary data events

EPICSTHREADFUNC spectra (zDDMRecord *psr)
this collects events into time and energy histograms

STATIC long zDDM_init(int after)
this initializes some stuff

STATIC long zDDM_init_record(struct zDDMRecord *psr, CALLBACK *pcallback)
this initializes things in the record

STATIC long zDDM_arm(void *psscal, int val)
this causes counting to start or stop.

STATIC long zDDM_reset(void)

STATIC long zDDM_write_preset(zDDMRecord *psr, int val)
this sets the count time.

void devzDDMConfig(int num_cards,       /* maximum number of cards in crate */
          int ndets,           /* Max. no. detectors */
          unsigned channels)   /* Max. no. channels */
int wrap(void *pscal)
this sets up hardware parameters

STATIC long zDDM_done(zDDMRecord *psr)
this checks to see if we are counting

void enable_scepter()
this turns on events from Scepter

int stuff_hermes(void *pscal)
this loads the SPI configuration data into the Hermes chips

int load_scepter(struct zDDMRecord *pdet, int regAddr, int chip)
this loads the SPI registers in one Scepter chip

int stuff_scepter(void *pscal)
this calls the above for each chip.

int load_ad9252reg(int addr, int data)

int ad9252_cnfg(int addr, int data)

int ldaddrlkup()
this loads the pixel map into the fabric/